## Slide 1
Real-time Gunshot Detection System Integration To Camera Surveillance Systems
A proactive approach to enhancing public safety through advanced technology.

## Slide 2
The Urgent Need for Gunshot Detection
Gun violence poses a grave threat to public safety, with escalating statistics highlighting the critical need for effective detection and alarming systems.
Escalating Violence
1,315 school shootings in the U.S. since 1970.
School Incidents
97 recorded shooting incidents at K-12 schools in 2018.
Firearm Fatalities
20,138 firearm deaths (excluding suicides) reported in 2022 alone.

## Slide 3
Limitations of Current Systems
Traditional gunshot detection systems face significant challenges in cost, coverage, and accuracy.
Prohibitive Costs
Acoustic systems average $65,000-$95,000 per mile annually, plus infrastructure and maintenance.
False Positives
Mistaking loud noises like firecrackers for gunshots, straining emergency resources.
ShotSpotter in Chicago sends police on 60+ false alarms daily.

## Slide 4
Our Proposed Solution: System Design
Our system seamlessly integrates with existing surveillance infrastructure, augmenting capabilities with real-time audio detection.
01
Microphone Inputs
Leverages pre-existing surveillance camera microphones. Three microphones enable sound source localization.
02
Audio Processing
Extracts Mel Frequency Cepstral Coefficients (MFCC) and other features from raw audio.
03
Machine Learning Model
Pre-trained model identifies gunshots from audio embeddings with high precision.
04
Alert Mechanism
Triggers immediate, flexible alerts to law enforcement, control centers, or audible alarms.

## Slide 5
Machine Learning Models for Gunshot Detection
We developed two distinct machine learning models for binary classification of gunshot audio.
YAMNet Transfer Learning
Utilizes TensorFlow's pre-trained YAMNet for sound embeddings, trained with a three-layered neural network.
Achieved over 99% accuracy in training, testing, and validation sets.
Audio MFCC Approach
Processes Mel-frequency cepstral coefficients (MFCCs) with a nine-layered model including an LSTM layer.
Demonstrated similarly high accuracy levels.

## Slide 6
Training Data: Gunshot & Non-Gunshot
Our models were trained on a diverse dataset of 3,200 samples each, ensuring robust classification.
Gunshot Data
851 audio files from Kaggle Gunshot Audio Dataset, featuring various firearms (e.g., AK-47, M16, MP5).
Pre-processed with resampling and power filtering to eliminate irrelevant audio.
Non-Gunshot Data
Approximately 3600 seconds of audio from YouTube, including thunder, fireworks, drums, and barks.
Underwent similar pre-processing, with no power threshold set.

## Slide 7
Hardware Implementation Strategies
We explore four hardware platforms for deploying our power-independent, autonomous system, balancing performance, power, and cost.
Microcontrollers
Compact, cost-effective, minimal power (milliwatt range), ideal for portable systems. Arduino boards ($20-$60).
Small Computers
Raspberry Pi ($35) offers more computational power than microcontrollers with low power consumption (2-3 watts).
FPGA
Field-Programmable Gate Arrays provide parallel processing for rapid, accurate detection. Higher cost ($100s-$1000s), but high performance.
Cloud-based Processing
Leverages remote data centers for complex algorithms, reducing local hardware needs. Highest accuracy, but ongoing costs.

## Slide 8
Model Performance: YAMNet vs. MFCC
Both models demonstrate high accuracy, with YAMNet showing slightly superior performance in validation and testing.
YAMNet Transfer Learning Model
Training Accuracy: 99.79%
Test Accuracy: 98.75%
Misclassifications: 5 non-gunshots as gunshots, 3 gunshots as non-gunshots (out of 1280 samples).
Audio MFCC-based Model
Training Accuracy: 99.84%
Test Accuracy: 96.95%
Misclassifications: 23 non-gunshots as gunshots, 16 gunshots as non-gunshots (out of 1280 samples).

## Slide 9
Key Insights & Trade-offs
Effective gunshot classification is achievable, but real-world deployment requires optimizing for efficiency.
1
Model Optimization
Focus on reducing model size while preserving high performance for smaller, power-efficient chips.
2
Computational Resources
YAMNet's superior accuracy may demand more computational resources, a key consideration for limited devices.
3
Balancing Factors
Crucial trade-offs exist between model size, computational needs, power consumption, and accuracy for optimal deployment strategies.

## Slide 10
Significance & Future Work
This research is a crucial step in mitigating gun violence, demonstrating the viability of machine learning for real-time threat detection.
Hardware Optimization
Further optimize model setup for each hardware configuration, ensuring high performance under stringent constraints.
Expanded Capabilities
Enhance recognition of diverse firearms and scenarios for broader real-world applicability.
Integrated Response
Integrate detection systems with emergency response units or multi-modal sensor data for enhanced accuracy.